## Slide 1
Origin-destination mobility flow inference from traffic data
Hungary
Mihály Hanics
CEU DNDS
Advisors: Márton Karsai, Gergely Ódor

## Slide 2: Current methods for ODM estimation
Inter-settlement origin-destination matrix
Problem: We would like to know how many people commute from a Hungarian city/town/settlement to others regularly.
Origin – destination pairs: For each location pair, the number of people travelling (commuting) between the two places over a time period (e.g. per day) is represented.
Usecases: Epidemic spreading modelling (our main interest), human mobility, traffic and traffic congestion prediction, human behaviour studies.
Challenges: Directly measured data is rare, inferring from certain types of data can raise other concerns (e.g. privacy)
Census data is only collected once over multiple years.
Goal: An alternative way to create Hungary’s O-D matrix with high accuracy and great resolution.
An example for an O-D matrix: rows represent
the origin locations, columns the destinations. The
stored value would equal the commuters inbetween

## Slide 3: Current methods for ODM estimation
Ground truth data from census
Commuting map in Hungary, from self-reported data [Ódor 2022]
Hungarian Central Statistical Office (KSH) 2016:
Data 1: Settlement statistics: population, latitude-longitude
Data 2: Commuting from one settlement to another:
  includes commuting to school, and to work
Both datasets include each settlement / pair of settlements where there is at least one commuter.
~3200 settlements, ~93000 pairs (non-zero commution)

## Slide 4: Current methods for ODM estimation
Observational data: Road traffic volume
Hungarian Public Roads 2022:
Nation-wide daily public road traffic measurements, average over a year
Vehicle, heavy vehicle, bicycle counts 14000 road segments, e.g. highways.
Geographical data
Some extra information on measurement

## Slide 5: Current methods for ODM estimation
Test network construction
Small network:
16 cities, 3 highway division points
Nodes represent the locations, edges are roads, possibly multiple roads
Weight: The minimum traffic volume on the road segments represented by the edge
Parallel edges may appear between two nodes (e.g. road 4 and highway M4), these are combined into one (sum)
„Proof of concept”
In accordance with the traffic data.

## Slide 6: Current methods for ODM estimation
Models - methods
Gravity [Parsons 1960]
where:
- : number of trips from zone to zone
- relate to the number of trips leaving location / attracted by location
- : the distance between zones i and
- deterrence: decreasing number of trips as the distance increases, by power-law
- : constant of proportionality
We use the scikit-mobility models to estimate an O-D matrix [Pappalardo 2022]
Bell [Bell 1983]
assuming
where contains the O-D pairs (-size column vector) (We infer it)
- : Traffic volumes – We measure it, input data (-size column vector)
-matrix: When travelling from A to B, how likely you are to pass through a certain road – This we pre-determine ( matrix)
road traffic, : probability of going through road given the O-D pair
Other methods optimize an objective function subject to constraints:
Bell-model: maximizes the probability of observing given initial probabilities
For us: estimated, , comes from the total trips sum

## Slide 7: Current methods for ODM estimation
Models - methods
Gravity [Parsons 1960]
where:
- : number of trips from zone to zone
- relate to the number of trips leaving location / attracted by location
- : the distance between zones i and
- deterrence: decreasing number of trips as the distance increases, by power-law
- : constant of proportionality
We use the scikit-mobility models to estimate an O-D matrix [Pappalardo 2022]
Bell [Bell 1983]
assuming
where contains the O-D pairs (-size column vector) (We infer it)
- : Traffic volumes – We measure it, input data (-size column vector)
- -matrix: When travelling from A to B, how likely you are to pass through a certain road – This we pre-determine ( matrix)
Other methods optimize an objective function subject to constraints:
Bell-model: maximizes the probability of observing given probabilities
For us: estimated, , comes from the total trips sum
(multinomial distribution)

## Slide 8
Bell-model in practice
Shortest paths - Between all pairs of locations, all shortest paths are computed.
For each of the N shortest paths between two locations, is added to a path’s edges
Some constraints in practice conflict -> use them as loss (L1 mostly)
assuming
Optimization:
assuming multinomial distributions
Bell:
Estimated by normalizing an initial guess:

## Slide 9: Current methods for ODM estimation
Gravity, Bell models pipeline

## Slide 10: Current methods for ODM estimation
Results on the small graph
 | Correlation | MSE | MAE | Relative diff^2 | Better prediction
Gravity | 95.8% | 62479 | ~124 | 1103 | 49
Bell from Gravity | 97.4% | 37298 | ~94 | 1138 | 71
Bell model improves on the initial model
This is true for the gravity model, but other tested models: entropy min/max. Superior especially in large O-D values.

## Slide 11: Current methods for ODM estimation
Next steps, future directions
Scale up the network to as large as we can: all roads, more settlements
Issues:
Technical issues e.g. different components (see figures on left)
The connected network from adding new edges and combining nodes.

## Slide 12: Current methods for ODM estimation
Next steps, future directions
Scale up the network to as large as we can: all roads, more settlements
Issues:
P-matrix creation: shortest path works weakly + we need multiple found paths

## Slide 13: Current methods for ODM estimation
Next steps, future directions
UPDATE:
Shortest time routes seem to work well.
One issue that came up is that now the used roads are „too crowded”-> low O-D value predictions

## Slide 14: Current methods for ODM estimation
Next steps, future directions
Scale up the network to as large as we can: all roads, more settlements
Issues:
Computation time: optimization ~46 sec for 16 locations, grows fast with more locations
  Network creation: finding intersections took 25 mins, overall procedure 30+ mins
Run the analysis for monthly traffic data between 2016 and 2022

## Slide 15: References
[Ódor 2021] Ódor G, Czifra D, Komjáthy J, Lovász L, Karsai M. Switchover phenomenon induced by epidemic seeding on geometric networks. Proceedings of the National Academy of Sciences. 2021;118(41):e2112607118. pmid:34620714
[Pappalardo 2022] Pappalardo, L., Simini, F., Barlacchi, G., & Pellungrini, R. (2022). scikit-mobility: A Python Library for the Analysis, Generation, and Risk Assessment of Mobility Data. Journal of Statistical Software, 103(1), 1–38.
[Parsons 1960] Parsons, Christopher R. ‘Do Migrants Really Foster Trade’. The Trade-Migration Nexus, a Panel Approach 2000 (1960).
[Bell 1983] Bell, M. G. (1983). The estimation of an origin-destination matrix from traffic counts. Transportation Science, 17(2), 198-217.
Data:
Nemzeti Adathozzáférési Pont – Magyar Közút Nonprofit Zrt.: Éves keresztmetszeti forgalmi adatok (2022)
https://napportal.kozut.hu/
Központi Statisztikai Hivatal - https://www.ksh.hu/